|  | ......................... pcs. .............................. € .............................. € GEZE overhead door closer system TS 5000 ISM with mechanical hold-open device, hold-open angle with precise variable adjustment between 80° and 130°, size 2 – 6, with integrated mechanical closing sequence control in accordance with EN 1158; hold-open position can be overridden, vandalism protection against wilful maloperation of the closing sequence control, closing force, closing speed, back check and latching action can be adjusted from the front, with visual closing force display, standard installation on door leaf/hinge side ( ) TS 5000 closer body size EN 2-6, up to leaf width 1400 mm, for barrier-free doors in accordance with DIN 18040, up to leaf width 1,100 mm ( ) TS 5000 ECline closer body size EN 3-5, with very high efficiency > 80% for barrier-free doors in accordance with DIN 18040, up to leaf width 1250 mm ( ) retrofit kit ECline ISM/ISM BG, opening assistance for use on the active leaf, considerable drop in opening torque Accessories: ( ) Integrated almost invisible flexible opening restrictor for E/R/ISM guide rails Colour: ( ) silver-coloured ( ) white ( ) stainless steel optic ( ) acc. to RAL |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE carry bar CB flex with GEZE door closer design, for guaranteeing the correct closing sequence for all 2-leaf GEZE door closer systems with door closing sequence control, length in installed state is infinitely variable adjustable (70 - 210 mm overhang), non-visible hinge and length adjustment mechanisms, with cover cap at the side, can be cut to size on site, painted surface as standard. Colour: ( ) silver-coloured ( ) acc. to RAL |