|  | ......................... pcs. .............................. € .............................. € GEZE Slimline fanlight opener OL 90 N Activation via electric linear drive E 212. For daily aeration and ventilation with electric linear drive on vertically installed rectangular windows with bottom-hung and top-hung casements, inward opening. Installation can be carried out from the front, without visible attachment screws. Casement is fitted with safety catch and locking device in the scissors. Casement closing pressure must be adjusted at the casement bracket. Variable stroke adjustment for simple regulation of the opening width For window cleaning, the scissors can be disengaged quickly by pressing the release catch. Rod must be covered using an aluminium profile. Activation must be using electric linear drive E 212. Technical data: Opening width: 170mm ( ) bottom-hung casement ( ) top-hung casement ( ) side-hung casement Drive installation: ( ) vertical at the side ( ) horizontal at the top ( ) E 212 R1/230 V AC With 1 relay for group switching via 1 operating spot/switch ( ) E 212 R/230 V AC With 2 relays for group switching via several operating spots/push button control ( ) E 212/24 V DC DC drive for 24V DC control units, including emergency power control units, suitable for RWA application Leaf width: ........ mm - With vertical drive installation ( ) 1 scissors for casement widths from 380 - 1200 mm1) ( ) 2 scissors for casement widths from 1201 - 2400 mm1) ( ) 3 scissors for casement widths from 2401 - 3600 mm1) - With horizontal drive installation ( ) 1 scissors for casement widths from 600 - 1200 mm1) ( ) 2 scissors for casement widths from 1201 - 2400 mm1) ( ) 3 scissors for casement widths from 2401 - 3600 mm1) 1) Heed panel widths Casement height: ........ mm (min. 250 mm with horizontal drive installation) (min. 500 mm with vertical drive installation) Space required at the side:........ mm (min. 35 mm with vertical drive installation) Space required at the top: .......... mm (min. 35 mm with horizontal drive installation Colour: ( ) silver-coloured EV1 ( ) white, 9016 ( ) RAL shade according to choice Note: When used on bottom-hung casements, we prescribe the use of separate safety scissors for product liability reasons. These represent an additional safety feature which guarantees the permanent connection of casement and frame, e.g. GEZE FPS. GEZE FPS gripping and cleaning scissors ( ) Size 1 from casement height 360 mm ( ) Size 2 from casement height 540 mm ( ) Size 3 from casement height 740 mm Note: When used on bottom-hung casements, we prescribe the use of separate safety scissors for product liability reasons. These represent an additional safety feature which guarantees the permanent connection of casement and frame, e.g. GEZE FPS. |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € Vent switch AS 500, for E 212 R ( ) with function buttons OPEN-STOP-CLOSE, for flush mounting ( ) optional surface mounting box |
|  | ......................... pcs. .............................. € .............................. € Fan switch AS 500, for E 212 R1 ( ) with function buttons OPEN-CLOSE, for flush mounting* |
|  | ......................... pcs. .............................. € .............................. € Vent switch AS 500, for E 212/24 V DC ( ) with function buttons OPEN-STOP-CLOSE, for flush mounting* alternatively, for surface mounting, please use surface-mounting box (ID 120503). |
|  | ......................... pcs. .............................. € .............................. € Installation and functional test Installation and functional test by an expert authorised by the manufacturer. |
|  | ......................... pcs. .............................. € .............................. € Start-up and official approval Official approval of the complete smoke and heat extraction system by an officially recognised expert, who also hands over the acceptance certificates. |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - compact package Maintenance and testing of hold-open systems (optional position) Service package for maintenance and testing according to ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - Fault diagnosis and repair jobs during the contract period will be carried out at reduced hourly rates - Service technicians will be deployed within 24 hours of the message being received from Monday – Friday between 7 am and 5 pm without surcharges - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 2 years |
|  | ......................... pcs. .............................. € .............................. € Service maintenance - comfort package Service maintenance (optional position) Comfort service package for maintenance and accident prevention inspection in accordance with ASR A1.7 as well as according to manufacturer’s specification with the following performance features: - Extension of the warranty to 36 months (condition: the maintenance contract is concluded 3 months after the commissioning date at the latest) - One maintenance per contract year - Free provision and updating of the test documents - Attachment of the inspection sticker - No separate charging for services and travel costs during the warranty period - No separate charging for consumables up to € 25 per maintenance - No separate charging for working hours when spare parts are replaced during the maintenance - Personal availability at the help desk 24 hours a day, 365 days a year - Contract run time: 3 years |
|  | ......................... pcs. .............................. € .............................. € Delivery and installation Wiring to be carried out on site by an electrical contractor according to the GEZE cable plan. Delivery, installation and commissioning through plant fitters or service partner. Safety analysis, instruction of the operator as to how the system works and handing over of the documentation. Annual maintenance and technical inspection by an expert authorised by the manufacturer incl. documentation of the inspection in an inspection log. |