|  | ......................... pcs. .............................. € .............................. € GEZE Slimline fanlight opener OL 95 Activation via spring hinge reverser with crank rod For daily aeration and ventilation on vertically installed casements, inward opening. Installation can be carried out from the front, without visible attachment screws. Casement is fitted with safety catch and locking device in the scissors. Casement closing pressure must be adjusted at the casement bracket. For window cleaning, the scissors must be able to be disengaged quickly by pressing the release catch. Rod must be covered using an aluminium profile. Technical data: Opening width: 220mm ( ) bottom-hung casement ( ) top-hung casement ( ) side-hung casement ( ) with corner operating gear Fz-90, left ( ) with corner operating gear Fz-90, right ( ) with gear Fz-91 for vertical installation ( ) with gear Fz-92 for angular and triangular windows ( ) with fixed crank rod ( ) with detachable crank rod Leaf width: ........ mm ( ) 1 scissors for casement widths from 440 - 1200 mm1) ( ) 2 scissors for casement widths from 1201 - 2400 mm1) ( ) 3 scissors for casement widths from 2401 - 2800 mm1) 1) Heed panel widths Casement height: ........ mm (min. 350 mm) Centre of rod to end Crank rod extended: ........ mm Colour: ( ) silver-coloured EV1 ( ) white, 9016 ( ) RAL shade according to choice Note: When used on bottom-hung casements, we prescribe the use of separate safety scissors for product liability reasons. These represent an additional safety feature which guarantees the permanent connection of casement and frame, e.g. GEZE FPS. |
| --- | --- |
|  | ......................... pcs. .............................. € .............................. € GEZE FPS gripping and cleaning scissors ( ) Size 1 from casement height 360 mm ( ) Size 2 from casement height 540 mm ( ) Size 3 from casement height 740 mm |